## Slide 1: Plugfest project – Shadow Proxy
Presenter
Ryuichi Matsukura, Fujitsu Limited

## Slide 2: Diagram in this plugfest
Fujitsu provides three services
  Sensor unit (temperature, humidity and air pressure)
  Proxy server
  Application
Proxy server
Sensor unit
192.168.30.xx
192.168.0.xx
Plugfest VPN
device
device
Application
(curl, nodeRED)
Fujitsu local
Internet
192.168.0.18
192.168.30.134
192.168.0.201
192.168.30.128

## Slide 3: Sensor unit
3 sensors: temperature, humidity and air pressure
ESP32 with Wi-Fi
Developed in C++ using Arduino
mDNS support

## Slide 4: Proxy server
Objectives
  prevent direct access to real devices.
  allow multiple devices connected with different protocols and authentication methods to connect using one protocol and one authentication method.
Shadow device
  are created on request from real device
  exposes the endpoint to applications instead of real device
Developed in JAVA on RaspberryPi (Linux)
Advertising the proxy address to real devices and applications with mDNS

## Slide 5: APIs of Proxy server
Registration and unregistration of shadow devices
Getting a list of registered shadows
Retrieving shadow TDs and real TDs
Search APIs are NOT implemented.
  APIs to search for devices with their description and attributes as a key

## Slide 6: Results: checked devices
4 devices are connected (Internet, VPN and local)
  Fujitsu sensor can find the proxy and register own TD to it automatically
  Others are register manually
  All devices can be controlled from the application on the VPN via the proxy
Proxy server
Sensor unit
192.168.30.xx
192.168.0.xx
Plugfest VPN
device
device
Application
(curl, nodeRED)
Fujitsu local
Internet
192.168.0.18
192.168.30.134
192.168.0.201
192.168.30.128
fjsensor(Fujitsu)
counter(Siemens)
hitachi-led(Hitachi)
temperaturesensor(ECHONET)