## Slide 1: Definitions about properties/actions/events
July 14, 2021
Ryuichi Matsukura
Fujitsu

## Slide 2: Introduction
How to integrate other platforms/protocols like LWM2M or IPSO.
Two primary models for API design: REST and RPC, for most software developers.
  gRPC vs REST: Understanding gRPC, OpenAPI and REST and when to use them in API design
  https://cloud.google.com/blog/products/api-management/understanding-grpc-openapi-and-rest-and-when-to-use-them
  REST vs RPC: What problems are you trying to solve with your APIs?
  https://cloud.google.com/blog/products/application-development/rest-vs-rpc-what-problems-are-you-trying-to-solve-with-your-apis

## Slide 3
From OCF 2.0.3 Specification overview slides.

## Slide 4
From OCF 2.0.3 Specification overview slides.
Properties
Actions

## Slide 5
“properties”: {
“Switch”: {
“type”: “boolean”,
“forms”: […]
},
“Brightness”: {
“type”: “number”,
“forms”: […]
},
},
“properties”: {
“Switch”: {
“type”: “boolean”,
“readOnly”: true,
“forms”: […]
},
“Brightness”: {
“type”: “number”,
“readOnly”: true,
“forms”: […]
},
},
“actions”: {
“SetSwitch”: {
“input”: {
“Switch”: “boolean”
},
{
“output”: {
“Switch”: “boolean”
},
“forms”: […]
},
“SetBrightness”: {
“input”: {
“Brightness”: “number”
},
{
“output”: {
“Brightness”: “number”
},
“forms”: […]
}
}
Definition with just properties
Definition with properties and actions

## Slide 6: Property vs. Action
Device defined by Properties can be easy to map to both Properties and Actions of WoT.
  LWM2M, NETCONF, and TR-069(BBF) are defined with Properties.
    These protocols are used in the device managements.
  OCF, KNX, BACnet, and ECHONET mainly defined with Properties.
Device defined by Actions CANNOT be easy to map to Properties of WoT unless if Input = Output.

## Slide 7: Events
“properties”: {
“Temperature”: {
“type”: “number”,
forms”; […]
}
}
“events”: {
“TemperatureChanged”: {
“Temperature”: {
“type”: “number”,
}
“forms”: […]
}
}
“properties”: {
“Temperature”: {
“type”: “number”,
“observable”; true,
“forms”; […]
}
}
Definition with just properties
Definition with properties and events

## Slide 8: Example: StorageBattery – ECHONET
Storage battery has 55 properties and 2 actions
https://echonet.jp/wp/wp-content/uploads/pdf/General/Download/web_API/ECHONET_Lite_Web_API_Dev_Specs_v1.3.0.pdf
Actions part
Properties part

## Slide 9
Actions part
Properties part